SMART MEDICINE DISPENSER

        Prepared By
        Urmila. S.R
        Preetha.S
        Neenu. M.S
    Vrinda. L

ABSTRACT

Frequent coordination between the physician and patient is time consuming, inconvenient, and poses a risk to the patient’s health by increasing the chances of error or a missed dose or extra dose. A real-time adaptive system needs to be developed. A smart medicine dispenser is a solution for this problem. The device must reliably dispense the medication in correct dosages with a success rate as close as possible to 100%. Device must be able to communicate with the physician via a computer interface and relay patient’s usage information. Device must be equipped with operating checks and alerts and must be easily refilled by the patient or the caretaker and tamper evident. Our device works according to the prescription entered by the doctor in a webpage designed for this purpose. The timing and dosage of each medicine is retrieved from the webpage using a gsm module and arduino and the medicines are dispensed accordingly. The heart rate sensor attached to the patient monitors his health and sends an alert to the preset mobile number in case of variations.

INTRODUCTION

        Most existing medication dispenser require users to configure the schedule and settings manually. This leads to inconvenience and errors due to mistyping. An error in a medication dispenser can have fatal consequences. Nonetheless existing medication dispensers are not equipped with remote device management functions. Therefore users should manage their MD by themselves. For example devices like ‘medtime’ provide only one medicine at a time and medication loading is difficult. 'compumed' dispenses only four times a day and its medicine cassette need to be changed weekly.
We are aiming at a device which can accept the prescriptions including the name of the medicine, its dosage and timing from the doctor. Pills are fed into the machine by a caretaker accordingly. The system sounds an alarm at the time preset by the doctor and the patient can get his medicine. There is a wearable connected to the device that senses the heart rate of the patient and alerts the doctor in case of any variations.The system has a provision for the doctor to change the dosage or even the medicine as required.

PROBLEM DEFINITION

Medication non adherence is a serious public health issue. Medically ignorant patients may take wrong dosage at wrong time. The rate of compliance with medication regimens in outpatient settings is generally regarded as poor. Even under the watchful eye of doctors, trained professionals working in a controlled setting make significant errors in the delivery of medication to patients. Compliance with such medication regimens have been shown to be worse after the patient leaves the hospital and the medication management is required to be performed by the patient or some other untrained family member.

GOALS AND OBJECTIVES

  - Reliable dispensing of medication.
  - Communication with physician through web interface.
  - Tamper evident device.

MODULES

Dispensing part
Arduino Board
- Servo motors
- 6v external power supply
- Cartridges for medicine storage
      The individual servo motors for each cartridge are connected to arduino. Power for the servo motors is provided by an external 6v supply.

Sensing part
- Heart rate sensor SPO2
- Arduino Promini
Heart rate sensor connected to arduino promini sends alert to doctor through a gsm module if there is any variation in the patient’s heart rate.

Communication Part

- GSM module
- Web page
GSM module is used to send alert to a preset mobile number as well as connect to the internet to provide communication between the webpage and the device.

SYSTEM REQUIREMENTS

HARDWARE
Arduino

Cartridges for storing pills

Servo motors

IR modules

GSM module

RF module

RTC DS3231

Relay board

Heart rate sensor

Arduino Pro mini

Jumper cables.

SOFTWARE

- Operating System : Linux Ubuntu
- Arduino IDE
- Programming Languages : Embedded C,HTML,CSS and php

CONCLUSION

The system mainly aims at helping the physically or mentally disabled patients in taking their medicines at the correct time in correct dosages. It incorporates arduino board with servo motors for the dispensing of medicines. The device works according to the prescription entered by the doctor through a webpage. This reduces the risk of taking wrong medicine at the wrong time. A wearable attached to the patient helps the doctor in monitoring his health condition so that doctor maybe alerted if there is a change in the patient’s heart rate. This will help to reduce medication non adherence.

REFERENCE
Accessed Controlled Pill Dispenser
        James Abrams,Vahe Barsoumian
Interactive Medication Dispenser
        Jonathan Breitbart,Kathleen Lu,Srikanth Narayan
Smart Medication Dispenser
        P. H. Tsai, C. Y. Yu, C. S. Shih, Member, IEEE, and J. W. S. Liu, Fellow, IEEE
Construction of a medication reminder synchronization system
        KeeHyun Part, Seung Hyeol Lin
Design of automatic mediaction dispenser
        S.Mukund,N.K.Srinath